## Slide 1
HART
Highway Addressable Remote Transducer
Soaib Ferdous
Md Arman Zaid Efty
Md Zulkar Nain Sayeed
Jamsadul Bari Fahad
B.Eng. Electronic Engineering · Hochschule Hamm-Lippstadt · Lippstadt, Germany
Industrial Communication Systems · Summer 2026

## Slide 2
What is HART?
A digital communication protocol for industrial field devices — built on top of the wiring that plants already use.
A smart-device protocol
Lets field instruments and the control system talk digitally.
Runs on existing 4–20 mA wires
No new cabling — it rides on the standard current loop.
Two signals at once
The analog reading and a digital conversation share one wire.
Carries diagnostics
Devices report not just a value, but their own health.
Question-and-answer model
The control system asks; each device answers in turn.
An industry standard
One of the most widely used protocols in process plants.
02

## Slide 3
The main idea, in one line
How HART fits in
HART works on existing 4–20 mA wiring.
The analog signal carries the process value.
The digital signal carries diagnostics and device data.
MAIN IDEA
HART helps check if the value is reliable.
03

## Slide 4
Industrial
Value of
HART
Why this protocol still matters on the plant floor
Uses existing 4–20 mA wiring
No new cabling required for retrofits.
Enables remote diagnostics
Device health is visible without a site visit.
Detects device faults early
Problems are flagged before they affect the process.
Supports maintenance planning
Feeds data into condition-based maintenance.
Improves process safety
Faults are caught sooner, reducing risk.
04

## Slide 5
How HART communicates
1
Control system sends a command
2
Field device sends a response
3
4–20 mA carries the process value
4
FSK digital signal carries device data
5
Status bytes report device health
6
Checksum verifies the frame
05

## Slide 6
What's inside a HART frame
Preamble
Start byte
Address
Command
Byte count
Status bytes
Data
Checksum
Field | Role
Preamble | Synchronization
Start byte | Request or response
Address | Selects device
Command | Tells action
Byte count | Data length
Status bytes | Device health
Data | Value or diagnostics
Checksum | Error check
Every HART response carries both data and fault information.
06

## Slide 7
How HART detects faults
HART detects errors using:
Status bytes
Checksum errors
No response
Timeout
Diagnostic commands
Analog / digital mismatch
This helps separate process problems from device problems.
07

## Slide 8
Practical applications of HART
Smart Transmitters
Temperature, pressure, flow
Reports PV and device health
Detects drift and calibration issues
Smart Valve Positioners
Actuator feedback and travel
Reports actual valve position
Finds valve sticking or stiction
DCS / PLC Integration
Plant-wide data collection
Polls field devices and collects diagnostics
Supports remote maintenance
08

## Slide 9
We put these ideas into a simulation
To see HART fault detection in action, we built a simple simulated control loop — a chemical reactor held at a target temperature by three HART devices.
Reactor · held at a steady temperature
TT-201
Measures the temperature
FT-202
Measures the inflow
FCV-203
Opens and closes the valve
09

## Slide 10
OUR PRACTICAL IMPLEMENTATION · 2 OF 4
Three simple problems, on purpose
We deliberately broke one thing at a time, to see whether HART would notice.
TT-201
The temperature sensor quietly gave a wrong reading.
FT-202
The flow sensor stopped responding entirely.
FCV-203
The valve did not move to where it was told.
10

## Slide 11
What we found
HART caught all three problems. Here's how long each one took to notice.
TT-201
Wrong reading
5.5
seconds
FT-202
No response
1.0
second
FCV-203
Valve stuck
0.0
seconds — instant
11

## Slide 12
Why it worked
HART's status bytes flagged every problem automatically —
before it could affect the process.
No one had to watch the reactor and notice a problem by eye. The same digital channel that carries the reading also carries the warning.
This is the same mechanism described earlier — just shown working on a real loop, end to end.
12

## Slide 13
Key
Takeaways
1
HART keeps 4–20 mA compatibility
2
Digital data adds device diagnostics
3
Status bytes help detect faults
4
CMD 3 detects sensor mismatch
5
CMD 48 detects valve position error
6
HART helps decide if data is trustworthy
13

## Slide 14
What we demonstrated
The concept holds up in practice
Everything explained about HART's frame and status bytes showed up exactly as described once we ran a real loop.
Three different faults, three different signatures
A wrong reading, a silent device, and a stuck valve each left a distinct, detectable trace.
Detection happened without raising the alarm ourselves
HART's own status bytes did the work — we only had to read them.
14

## Slide 15
HART vs. other fieldbus protocols
Attribute | HART | Found. Fieldbus | PROFIBUS PA
Reuses 4–20 mA wiring | Yes | No | No
Keeps the analog signal | Yes | No | No
Device diagnostics | Yes | Yes | Yes
Easy to retrofit | High | Low | Low
Installed base | Very large | Smaller | Smaller
Why HART wins
It adds digital diagnostics without throwing away the analog wiring already in place.
That makes it the easiest protocol to adopt in an existing plant — the reason it is so widely used.
15

## Slide 16
Thank you
Questions & discussion welcome
HART-Based Fault Detection in a Reactor Temperature Control Loop
Soaib Ferdous · Md Arman Zaid Efty · Md Zulkar Nain Sayeed · Jamsadul Bari Fahad
Hochschule Hamm-Lippstadt · Industrial Communication Systems